## Slide 1
Enhancing Protein Extraction from Faba Beans:
The Role of Pressure-Cooking Pretreatment
Dilara Özcan1
Prof. Dr. Özlem ÖZMUTLU KARSLIOĞLU2, Prof. Dr. Mecit Halil ÖZTOP1*
1Department of Food Engineering, Middle East Technical University, Ankara,Turkey
2Institute of Food Technology, University of Applied Sciences Hochshule Weihenstephan-Triesdorf, Freising, Germany

## Slide 2
OUTLINE
Introduction
Objective of the Study
Materials & Methods
Results & Discussion

## Slide 3
INTRODUCTION

## Slide 4
Consumer interest:
  Reduced saturated fat intake
  Heightened awareness of sustainable food production
  Ethical concerns about animal treatment
  Higher protein intake is advantageous.
Various plant-based protein sources
  Cereals
  Legumes
  Pseudocereals
  Nuts, almonds, and seeds
Plant-Based Proteins and Their Sources
(Hertzler et al., 2020)

## Slide 5
Why Faba Bean?
  It is a good protein source for extraction of proteins because of
    its low cost
    less allergenicity
    high protein content (lysine rich)
    Low lipid content (1%)
  Lack of studies exploring innovative pre-treatment processes for faba bean protein concentration.
    pressure cooking
(“Faba Bean: Chemistry, Properties and Functionality,” 2022)

## Slide 6
OBJECTIVE OF THE STUDY

## Slide 7
  Develop high-protein faba bean concentrates for plant-based diets.
  Enhance protein yield and solubility through pressure-cooking pretreatment.
  Compare the effects of pH and temperature on alkaline extraction efficiency.
  Optimize protein extraction conditions to enhance yield and solubility.
    Central Composite Design within Response Surface Methodology (RSM)
  Evaluate the functional properties of the best-performing product and its counterpart to assess overall quality and suitability for various applications.

## Slide 8
MATERIALS & METHODS

## Slide 9
No Pretreatment
Milled Faba Bean Powder
Mix sample with distilled water (1:10 (g/mL))
put on shaker (130 rpm) for 16h
Cooking with Pressure Cooker
(3 min)
Adjusting pH with 1M NaOH
(pH 6-9-12)
Shaking at controlled temperatures in a water bath shaker
(30-45-60 °C)
Re-adjusting pH with 1M NaOH
(pH 6-9-12)
Put into centrifuge
(2263 x g for 15 min)
Collect supernatant, discard precipitate
Collect Supernatants
Apply Bradford Assay to check soluble protein & collect datas
Optimization of best production method with the help of RSM
Optimization of Protein Extraction from Faba Bean

## Slide 10
Optimization Parameters:
Pretreatment
  No Pretreatment
  Pressure Cooking (3 min)
pH Adjustment
  pH 6
  pH 9
  pH 12
Extraction Temperature
  30 °C
  45 °C
  60 °C
  Central Composite Design is selected with 2 continuous & 1 categorical factors (α = 1)
  Soluble Protein Content will be used as response (Bradford Assay will be used).

## Slide 11
Characterization Experiments:
WHC-OHC
Soluble Protein Content
Color Analysis
Foaming Properties
Total Protein Content
Color Analysis

## Slide 12
RESULTS & DISCUSSION

## Slide 13
Although temperature does not appear to have a strong individual effect based on the main effects plot, the interaction between temperature and pretreatment is identified as significant in the normal plot of standardized effects, suggesting a combined influence on protein solubility.
Optimization Results:

## Slide 14
Hold Values: No Pretreatment
Hold Values: Pressure Cooking
Without pretreatment, the combination of high pH and low temperature increases protein solubility by up to 75%, whereas when pressure cooking is applied, solubility is limited to 20%,
pretreatment negatively affects protein structure.

## Slide 15
FACED PROBLEM IN PRESSURE COOKING PROCESS:
Starch Gelatinization of Faba Bean Solution:
collected sample from the pressure cooker
after cooling to room temperature
"Starch gelatinization,
occurs due to heat and pressure in the pressure cooker.
Starch granules absorb water, swell, and lose their crystalline structure.
A gel matrix forms, which traps the proteins."
Impact on protein extraction:
Proteins become difficult to recover, significantly hindering protein extraction efficiency.
(Chen & Smith, 2023).

## Slide 16
Temperature | pH | Preatment | Protein Solubility (%)
30 | 11.64 | No | 73.81 ± 4.17
The goal of the optimization process was to identify the conditions yielding the highest protein solubility.
Through the Response Surface Methodology (RSM), it was determined that the optimal conditions are a pH of 11.64 and a temperature of 30°C without any pretreatment, achieving a predicted protein solubility of 74.28%.
This result highlights the significant influence of pH and temperature on protein solubility in the absence of pretreatment.
For experimental verification of the conditions obtained as a result of optimization, soluble protein was validated by Bradford assay at optimum conditions.

## Slide 17
RSM
Conducted
Verification
Full-Scale Production
Pretreatment Assessment
Comparative Analysis
Optimal conditions identified:
  pH 11.64
  30°C
  without pretreatment
Experiments confirmed the optimal result.
Final product obtained by adjusting pH to 4 (isoelectric point).
Pressure-cooked version produced under identical conditions.
Both products prepared for detailed comparison.

## Slide 18
Sample | Total Protein Content (%) (g protein/g dry sample) | Protein Recovery Yield (%) (g product protein/g sample protein)
Milled Faba Bean (Raw Material) | 23.55 ± 0.16C | -
Optimum Product | 68.44 ± 1.72A | 53.27 ± 1.34A
Pressure Cooked Product Under Optimum Conditions | 60.94 ± 0.30B | 23.43 ± 0.12B
Comparative Functional Analysis of the Optimal Product and Pressure Cooking Pretreated Product
Total Protein Content (Kjeldahl Method) & Recovery Yield (%):
The protein content in the pressure-cooked product is lower compared to the standard optimal product, and the recovery yield significantly decreases.

## Slide 19
Sample | Soluble Protein Content (g soluble protein/g total protein) (%)
Milled Faba Bean (Raw Material) | 0.17 ± 0.09C
Optimum Product | 1.48 ± 10.13B
Pressure Cooked Product Under Optimum Conditions | 2.49 ± 0.23A
Soluble Protein Content (Bradford Assay):
The soluble protein content is higher in the pressure-cooked product compared to the optimal product, showing a significant increase.
Notes: The increase in soluble protein content in the pressure-cooked product could be due to the pressure treatment causing protein denaturation and unfolding. This process exposes hydrophilic groups and enhances the solubility of proteins, making more protein available in the soluble fraction. Additionally, the heat and pressure may break down protein aggregates, further increasing solubility.

## Slide 20
Water Holding & Oil Holding Capacity:
Sample | WHC (g H2O/g sample) | OHC (g oil*/g sample)
Milled Faba Bean (Raw Material) | 3.27 ± 0.26C | 2.51 ± 0.10A
Optimum Product | 3.66 ± 0.03B | 2.47 ± 0.22A
Pressure Cooked Product Under Optimum Conditions | 4.65 ± 0.03A | 2.90 ± 0.33A
*For oil holding capacity determination experiment, sunflower oil is used.
The pressure-cooked one shows a higher water holding capacity compared to the optimum product, with a slight increase in oil holding capacity as well.

## Slide 21
Color Analysis:
Sample | L* | a* | b*
Milled Faba Bean (Raw Material) | 82.43 ± 0.68A | 1.63 ± 0.31C | 14.77 ± 0.90A
Optimum Product | 53.20 ± 0.46C | 7.40 ± 0.10A | 12.03 ± 0.25B
Pressure Cooked Product Under Optimum Conditions | 59.37 ± 0.23B | 6.77 ± 0.06B | 11.50 ± 0.17B
Milled Faba Bean Powder
11.64 pH /30 C/ without pretreatment product
11.64 pH /30 C/ pressure cooked product
The pressure-cooked product shows
  Increase in lightness (L*) compared to the optimal product, indicating a brighter color
  The redness (a*) and yellowness (b*) values slightly decrease.
These changes suggest that the pressure cooking treatment leads to a lighter and less intense color profile compared to the standard optimal product.

## Slide 22
Foaming Properties:
Sample | FC (%) | FS (%)
Milled Faba Bean (Raw Material) | 65.28 ± 4.81B | 41.08 ± 3.51B
Optimum Product | 83.33 ± 0.07A | 63.33 ± 1.44A
Pressure Cooked Product Under Optimum Conditions | 81.39 ± 3.37A | 61.11 ± 3.15A
Improved foaming capacity (FC) in both products compared to raw material.
Slight reduction in FC for pressure-cooked product but still high.
Similar foaming stability (FS) between optimal and pressure-cooked products.

## Slide 23
CONCLUSION:
Pressure cooking process had a negative effect on final product protein content but this pretreatment can increase functional properties.
Heat and pressure reduce the yield of the final product.
  From a sustainability perspective, additional energy for these processes is unnecessary.
Future research will consider these findings and explore more efficient and sustainable methods.

## Slide 24
REFERENCES:
Faba Bean: Chemistry, Properties and Functionality. (2022). In Faba Bean: Chemistry, Properties and Functionality. Springer International Publishing. https://doi.org/10.1007/978-3-031-14587-2
Hertzler, S. R., Lieblein-Boff, J. C., Weiler, M., & Allgeier, C. (2020). Plant proteins: Assessing their nutritional quality and effects on health and physical function. In Nutrients (Vol. 12, Issue 12, pp. 1–27). MDPI AG. https://doi.org/10.3390/nu12123704
Chen, J., & Smith, R. (2023). Starch Gelatinization and Its Impact on Protein Extraction. In Advances in Food Science and Technology (pp. 45-67). Springer. https://link.springer.com/chapter/10.1007/978-981-19-4796-4_3

## Slide 25
ACKNOWLEDGEMENT
This study has received funding from the European Union's Horizon 2020-PRIMA Section I Program under grant agreement #2232 (ProxIMed)

## Slide 26
THANK YOU!

## Slide 27
Central Composite Design (α = 1):
After all, data collected RSM is applied.
Despite the high R2 values and the absence of unusual observations in the model, the normality test yielded a p-value lower than 0.01.
Therefore, a Box-Cox transformation was applied to the data.

## Slide 28
Method
Box-Cox transformation λ = 0
After applying the Box-Cox transformation, the data showed a normal distribution, and the p-value in the normality test exceeded 0.1, indicating that the model meets the normality assumption.

## Slide 29
  Known as horse, broad, tick beans, or fava when green.
  Ranks third after soybean and pea in food legumes.
Main producers:
    China (36.7%)
    Ethiopia (20.1%)
    UK and Australia (8.2% each)
  Ancient, diverse legume with high nutrition.
Faba Bean (Vicia faba L.)
  Green, dried, roasted, soaked, frozen, cooked, canned.
Nutrient Rich:
  Lysine, proteins, minerals, vitamins, Levodopa (dopamine precursor).
Dietary Protein:
  Affordable in underdeveloped nations
    (Africa, Latin America, Asia).
Macronutrient Profile:
  51-68% carbohydrates
  20-41% protein
    Albumins 20%,
    Globulins 60%
    Glutelins 15%,
    Prolamins 8%;
    globulins (legumin, vicilin) important for protein composition.
(Langton et al., 2020)
(“Faba Bean: Chemistry, Properties and Functionality,” 2022)