## Slide 1
Dilara Özcan1
Assoc. Prof. Emin Burçin ÖZVURAL2 Prof. Dr. Özlem ÖZMUTLU KARSLIOĞLU3, Prof. Dr. Mecit Halil ÖZTOP1*
1Department of Food Engineering, Middle East Technical University, Ankara,Turkey
2Department of Food Engineering, Çankırı Karatekin University, Çankırı,Turkey
3Institute of Food Technology, University of Applied Sciences Hochshule Weihenstephan-Triesdorf, Freising, Germany
Impact of Pretreatment Methods on
Protein Extraction Efficiency and Functional Properties of Faba Beans

## Slide 2
OUTLINE
Introduction
Objective of the Study
Materials & Methods
Results & Discussion

## Slide 3
INTRODUCTION

## Slide 4
Interest in plant-based proteins is rising due to growing concerns about health, sustainability, and animal welfare.
Various plant-based protein sources
  Cereals
  Legumes
  Pseudocereals
  Nuts, almonds, and seeds
Among these sources, faba bean (Vicia faba L.) stands out as a promising candidate due to its nutritional and functional potential.
Plant-Based Proteins and Their Sources
(Hertzler et al., 2020)
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 5
Faba Bean (Vicia faba L.)
  Ancient, diverse legume with high nutrition.
  Known as horse, broad, tick beans, or fava when green.
  Ranks third after soybean and pea in food legumes.
Main producers:
  China (36.7%)
  Ethiopia (20.1%)
  UK and Australia (8.2% each)
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 6
Faba Bean (Vicia faba L.)
Green, dried, roasted, soaked, frozen, cooked, canned
Nutrient-rich:
  Lysine, proteins, minerals, vitamins, Levodopa (dopamine precursor).
Dietary protein:
  Affordable in underdeveloped nations
    (Africa, Latin America, Asia).
Macronutrient profile:
  51-68% carbohydrates
  20-41% protein
    Albumins 20%,
    Globulins 60%
    Glutelins 15%,
    Prolamins 8%;
    globulins (legumin, vicilin) important for protein composition.

## Slide 7
Why Faba Bean?
  It is a good protein source for extraction of proteins because of
    its low cost
    high protein content (lysine rich)
    Low lipid content (1%)
  Lack of studies exploring innovative pre-treatment processes for faba bean protein concentration.
    pressure cooking
    bleaching
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 8
Bleaching
Faba bean proteins may contain pigments (e.g., tannins, phenolics) that affect color and functionality.
Bleaching (e.g., with hydrogen peroxide) is used to:
  Reduce unwanted pigments and off-colors
  Improve whiteness and purity of protein concentrates
  Enhance consumer acceptability for food applications
It can assist in breaking the seed matrix, improving protein release during extraction.
Must be carefully optimized to avoid protein degradation or nutritional loss.
Commonly used in soy and legume protein processing
(Aider et al., 2012; Boye et al., 2010)
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 9
with Bleaching
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 10
OBJECTIVES OF THE STUDY

## Slide 11
  Investigate the effect of different pretreatments on faba bean protein obtained by alkaline extraction.
    bleaching, pressure cooking, and a combination of the them
  Evaluate the effects of pretreatments on protein yield, soluble protein content, and total protein content.
  Analyze color differences and structural changes between samples using FTIR spectroscopy.
  Evaluate the basic functional properties of protein concentrates, such as protein solubility, water/oil holding capacity, and foaming ability.
  Compare the best-performing sample with a commercial protein product to examine its quality and potential applications.

## Slide 12
MATERIALS & METHODS

## Slide 13
Bleaching Process
Put suspension to stirrer for 30 min
Place the solution in a tray dryer (60 C) until completely dry
Mix ground sample with 3% Hydrogen Peroxide Solution
(1:10 g/mL)
Grind the sample
by grinder
Faba Bean
Grind the sample
by grinder
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 14
Protein Extraction from Faba Bean
No Pretreatment
Milled Faba Bean Powder
Mix sample with distilled water
put on shaker overnight
Cooking with Pressure Cooker
(5 min)
Adjusting pH with NaOH & put on shaker for 2 h
Adjust pH to isoelectric point of sample
(4 pH)
put on stirrer for 1 h
Put into centrifuge
(2263 x g for 15 min)
Collect precipitate, discard supernatant
Adjust pH to 7
with NaOH
Put into freezer (-80 °C)
Freeze dryer
for 48 days
Put into centrifuge
(2263 x g for 15 min)
Collect supernatant, discard precipitate
Collect samples
Milled & Bleached Faba Bean Powder
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 15
Characterization of Protein Products:
WHC-OHC
Soluble Protein Content
Color Analysis
FTIR
Foaming Properties
Total Protein Content
Color Analysis

## Slide 16
RESULTS & DISCUSSION

## Slide 17
Comparative Functional Analysis of Proteins Obtained from Different Pretreatments
Total Protein Content (Kjeldahl Method) & Recovery Yield (%):
Groups with different letters are significantly different according to Tukey’s HSD test (p < 0.05).
CP had the highest recovery yield, while BP showed higher protein content, suggesting bleaching improved extractability.
PC lowered both values, due to heat-induced denaturation.
B-PCP showed the lowest performance; during its preparation, gel formation was observed, which hindered protein extraction.
CFP had the highest protein content, serving as a commercial benchmark, while BP showed a comparable value, indicating its potential as an alternative.
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 18
Sample | Soluble Protein Content (g soluble protein/g total protein) (%)
RF | 1.69 ± 0.891c
CP | 67.44 ± 6.85A
PCP | 14.85 ± 0.20BC
BP | 77.78 ± 8.06A
B-PCP | 22.53 ± 0.99B
CFP | 14.42 ± 1.86BC
Soluble Protein Content (Bradford Assay):
BP showed the highest solubility, slightly higher than CP, indicating improved dispersibility through bleaching..
CP also performed well, confirming that alkaline extraction without pretreatment is effective for solubility.
Both PCP and CFP exhibited similarly low solubility, suggesting that thermal and industrial processing might reduce functional protein regions.
RF, as expected from the untreated flour, had the lowest solubility, underlining the need for extraction.
BP exhibited the greatest solubility, performing better than CP, likely due to structural changes after bleaching..
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 19
Water Holding & Oil Holding Capacity:
*For oil holding capacity determination experiment, sunflower oil is used.
CP showed the highest WHC, while CFP and PCP also performed well in water holding.
BP and B-PCP had the lowest WHC, likely due to structure disruption and gel formation.
In terms of OHC, PCP showed the highest value, suggesting improved oil interaction through heat.
B-PCP and RF exhibited the lowest OHC, indicating limited oil holding capacity.
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation
Notes: Combination of pretreatments has a negative effect on WHC and OHC.

## Slide 20
Color Analysis:
Sample | L* | a* | b*
RF | 82.43 ± 0.68c | 1.63 ± 0.31c | 14.77 ± 0.90b
CP | 52.30 ± 0.52e | 6.23 ± 0.32a | 9.63 ± 0.41c
PCP | 53.80 ± 0.76d | 5.88 ± 0.29a | 9.35 ± 0.30c
BP | 87.63 ± 0.42a | 1.27 ± 0.12c | 5.50 ± 0.72d
B-PCP | 81.87 ± 0.45c | 2.93 ± 0.15b | 20.33 ± 0.21a
CFP | 85.60 ± 0.10b | 1.23 ± 0.06c | 15.33 ± 0.23b
BP had the highest L* value, indicating effective bleaching that resulted in the lightest appearance among samples.
Its color profile was closest to CFP, showing that bleaching helped approach commercial whiteness.
CP and PCP had lower L* and higher a* values, reflecting pigment retention and darker, reddish tones.
B-PCP showed increased yellowness (b*), likely due to Maillard-type browning during combined treatments.
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 21
Bleaching significantly improved the visual brightness of the protein powders. The bleached sample (BP) appeared closest to commercial whiteness, while control (CP) and PCP samples retained a visibly darker, brownish color due to remaining pigments. The B-PCP sample showed a slight greenish tone, possibly from pigment-heat interaction.
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation
Milled Faba Bean Powder
Faba Bean Protein (Control)
Pressure Cooked Faba Bean Protein
Bleached Faba Bean Protein
Bleached & Pressure Cooked Faba Bean Protein
Commercial Faba Bean Protein

## Slide 22
Foaming Properties:
CFP showed the highest foam capacity (FC), likely due to its purified and highly soluble protein structure.
BP had both high FC and the highest foam stability (FS), indicating bleaching positively affected foam quality.
B-PCP had the lowest FS, likely due to gelation or aggregated proteins disrupting foam film formation.
CP and PCP showed moderate foaming performance, while RF remained limited in both FC and FS due to lack of extraction.
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation

## Slide 23
FTIR:
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation
The Amide I band (~1650 cm⁻¹), related to protein secondary structure, was most pronounced in the commercial and control samples, indicating more ordered structures.
The bleach sample showed moderate intensity, while Bleach-PC had the weakest signal, suggesting protein denaturation or aggregation due to combined treatment. These structural differences align with the functional properties observed.

## Slide 24
CONCLUSION:
The PRIMA programme is supported under Horizon 2020, the European Union’s Framework Programme for Research and Innovation
Among the pretreatments, bleaching (BP) consistently improved protein quality, with high protein content, solubility, and foam stability, while also yielding a lighter color similar to the commercial sample.
Although CP (control) showed the highest recovery yield and good water/oil holding capacity, its darker color and lower protein solubility compared to BP may limit its application in some food systems.
PCP enhanced OHC but decreased protein quality overall, likely due to heat-induced denaturation.
B-PCP resulted in the poorest performance, possibly due to gel formation and structural damage during combined treatment.
Overall, bleaching alone proved to be the most effective pretreatment, producing a protein concentrate that closely resembled the commercial product in terms of both composition and functionality.

## Slide 25
ACKNOWLEDGEMENT
This study has received funding from the European Union's Horizon 2020-PRIMA Section I Program under grant agreement #2232 (ProxIMed)

## Slide 26
REFERENCES:
Chen, J., & Smith, R. (2023). Starch Gelatinization and Its Impact on Protein Extraction. In Advances in Food Science and Technology (pp. 45-67). Springer. https://link.springer.com/chapter/10.1007/978-981-19-4796-4_3
Faba Bean: Chemistry, Properties and Functionality. (2022). In Faba Bean: Chemistry, Properties and Functionality. Springer International Publishing. https://doi.org/10.1007/978-3-031-14587-2
Hertzler, S. R., Lieblein-Boff, J. C., Weiler, M., & Allgeier, C. (2020). Plant proteins: Assessing their nutritional quality and effects on health and physical function. In Nutrients (Vol. 12, Issue 12, pp. 1–27). MDPI AG. https://doi.org/10.3390/nu12123704

## Slide 27
THANK YOU!